## Slide 1: Reducing Onboard Processing Time for Path Planning in Dynamic Environments
Presentation by Group 10
    Aman Singh
    Aditya Shirwatkar
    Jana Ravi Kiran
TA and Mentor
    Ajay Kumar Sandula
Reference: M. Missura, D. D. Lee and M. Bennewitz, "Minimal Construct: Efficient Shortest Path Finding for Mobile Robots in Polygonal Maps," 2018 IEEE/RSJ International Conference on Intelligent Robots and Systems (IROS), Madrid, Spain, 2018, pp. 7918-7923, doi: 10.1109/IROS.2018.8594124.

## Slide 2: Agenda
Motivation
Introduction
Literature Overview
Implementation
Results and Discussion
Scope of Future Work
Agenda

## Slide 3: Motivation
Autonomous agents face the challenge of coordinating multiple tasks (perception, motion planning, controller) on a single onboard computer
All these tasks are computationally expensive
This work focuses on reducing onboard processing time for global path planning in polygonal maps.
Motivation
Image Source: https://techxplore.com/news/2020-04-framework-indoor-robot-humans.html

## Slide 4: Introduction
Traditional way of finding the shortest path
  Grid based maps (blocked, free or unknown)
  Search using A* or Djikstra's algorithms
Advantages of polygonal maps
  Less time complexity
  Less memory foot-print
  Well suited to represent moving obstacles
  Not prone to pitfalls of discretization
Introduction

## Slide 5: Literature Review
Construction Visibility Graph
  More time consuming than search
  Not suitable for changing environments (repair or reconstruction)
Time Complexity
  Upper Bound - O(n2)
  Lower Bound - Ω(n2)
Reference: M. Missura, D. D. Lee and M. Bennewitz, "Minimal Construct: Efficient Shortest Path Finding for Mobile Robots in Polygonal Maps," 2018 IEEE/RSJ International Conference on Intelligent Robots and Systems (IROS), Madrid, Spain, 2018, pp. 7918-7923, doi: 10.1109/IROS.2018.8594124.
Literature Review

## Slide 6
Construction Visibility Graph
  Compute only necessary portion during A* search
  Graph edges are only checked for intersection with polygons when they are popped from the priority queue
  Exploiting the fact that concave corners and non-tangential edges can never be a part of shortest path
Time Complexity
  Upper Bound - O(n2)
  Lower Bound - Ω(n)
Reference: M. Missura, D. D. Lee and M. Bennewitz, "Minimal Construct: Efficient Shortest Path Finding for Mobile Robots in Polygonal Maps," 2018 IEEE/RSJ International Conference on Intelligent Robots and Systems (IROS), Madrid, Spain, 2018, pp. 7918-7923, doi: 10.1109/IROS.2018.8594124.
Literature Review
Literature Review: Minimal Construct Algorithm

## Slide 7: Implementation
Used MATLAB Robotics Toolbox
Global Path planning:
  Used Minimal Construct Algorithm to give shortest global path
  Compared its computation time against the Grid based A* algorithm
Control:
  Used pure pursuit controller to follow the global paths
Code:
  https://github.com/aditya-shirwatkar/CP230_HWS
Implementation

## Slide 8: Implementation: Flowchart
Implementation

## Slide 9: Minimal Construct Algorithm: Preliminaries
Neighborhood: All the nodes connected through an edge
Closed node: If algo reaches a node we call it closed node
Parent: The closest, closed node in the neighborhood
Convex vertices of Polygon: All the vertices which form an external angle greater than 180°
Tangential point: Point Vj is tangential w.r.t Vi if, Vj+1 and Vj-1 are on the same side of the line Vi-Vj
Implementation
Reference: M. Missura, D. D. Lee and M. Bennewitz, "Minimal Construct: Efficient Shortest Path Finding for Mobile Robots in Polygonal Maps," 2018 IEEE/RSJ International Conference on Intelligent Robots and Systems (IROS), Madrid, Spain, 2018, pp. 7918-7923, doi: 10.1109/IROS.2018.8594124.

## Slide 10: Minimal Construct Algorithm: Overview
Implementation

## Slide 11: Minimal Construct Algorithm: Example
Implementation

## Slide 12: Minimal Construct Algorithm: Example
Implementation

## Slide 13: Minimal Construct Algorithm: Line Intersection Test
Literature Review
Implementation
Divide the line segment into sub-line segments using intersection points with the polygon.
Check if any midpoint of the sub-line segments lies inside the polygon.
If yes, the line segment intersects the polygon. If not, it doesn't intersect the polygon.
Image Source: https://www.codeproject.com/Articles/371959/A-brute-force-approach-to-check-if-a-line-segment

## Slide 14: Pure Pursuit Controller
The controller calculates a lookahead point on the desired path and determines the steering angle required to guide the robot towards that point.
The steering angle is calculated based on the pursuit angle, which is the angle between the robot's heading and a line connecting the robot's position to the lookahead point.
Image Source: https://in.mathworks.com/help/nav/ug/pure-pursuit-controller.html
Implementation

## Slide 15: Dynamic Office Environment (Case 1):-
A* grid
Minimal Construct
Results

## Slide 16: Dynamic Office Environment (Case 2):-
A* grid
Minimal Construct
Results

## Slide 17: Dynamic Office Environment (Case 3):-
A* grid
Minimal Construct
Results

## Slide 18: Dynamic Office Environment (Case 4):-
A* grid
Minimal Construct
Results

## Slide 19: Comparison
Recomputed time (sec)​ | Minimal Construct | A* Grid
Case 1 | 0.72428 0.70226 | 2.862 2.4654
Case 2 | 0.72056 0.38755 | 3.4207 1.7273
Case 3 | 0.66066 0.37973 | 2.9466 1.9843
Case 4 | 0.59119 0.27378 | 2.8302 1.4022
Results
Total Time taken to Reach Goal

## Slide 20: Scope for future work
  Robust Local planner for obstacle avoidance
  Code optimization in C++
  Implementation to different real-world scenarios
  Extension to 3D polytopes for UAVs, if possible
Future Work
Notes: such as moving people and objects, opening and closing doors, or simply the exploration of an unknown part of the map,

## Slide 21: Thank You!

## Slide 22: Problems Faced
Line Intersection Test
  Most computationally expensive function
  Could not implement a generalized version
Generating a dynamically evolving map
Implementation

## Slide 23: Visibility graph